http://www.b2c-shopping.co.uk

INSTRUCTIONS MANUAL

- Plug the AC power adapter in a wall outlet.

- Connect the AC power adapter supplied with your charger to the DC in jack.

- “STATUS” indicator shows RED when the charger is ready and “charger” indicator shows flashing GREEN when waiting for battery pack.

- Slide battery pack in the Charger and “CHARGER” indicator goes RED when charging.

- “CHARGE” indicator shows RED and GREEN alternatively when battery pack has more than 90% charged.

- When the battery pack is fully charged, the “CHARGE” indicator shows a steady green.

- After the battery pack fully charged, slide the battery pack out.

- Unplug DC power, “CHARGE” and “STATUS”indicators go out.

ADDITIONAL SAFETY INSTRUCTIONS FOR YOUR CHARGER

- If the charger supply cord is damaged have it replaced by a qualified person.

- Do not charge a leaking battery.

- Do not use machines, attachments and chargers for works other than those for which they are designed.

- Only connect the charging device to an AC supply.

- Only charge batteries with the appropriate charging device - as specified in these instructions.

- The charger must be protected from moisture.

- Do not use the charger outside.

- Do not short out the contacts of charger.

- Respect the polarity “+/-” when charging.

- When charging batteries, ensure that the battery charger is in a well-ventilated area and away from flammable materials. Batteries can get hot during charging. Do not overcharge any batteries. Ensure that batteries and chargers are not left unsupervised during charging.